/*

Remote login

Client

*/

#include <netdb.h>

#include <stdlib.h>

#include <stdio.h>

#include <string.h>

#include <termio.h>

#include <unistd.h>

#include <netinet/in.h>

#include <sys/socket.h>

#include <sys/types.h>

#define BUFFSIZE 512

struct termio cli_termio;

struct termio tty_mode;

void pass_all(int fd);

int tty_raw(int fd);

int tty_reset(int fd);

int tty_getmode(int fd, struct termio *tty_termio);

int main( int argc, char *argv[])

{

int sd,ret;

char buff[20]="hello server";

char buff1[50];

struct sockaddr_in servaddr;

/*creat a socket*/

if((sd=socket(AF_INET,SOCK_STREAM,0))==-1)

{

perror("socket fail");

exit(1);

}

bzero((struct sockaddr*)&servaddr,sizeof(servaddr));

servaddr.sin_family=AF_INET;

servaddr.sin_port=htons(atoi(argv[1]));

servaddr.sin_addr.s_addr=inet_addr(argv[2]);

/*connect the socket with the server*/

if(connect(sd,(struct sockaddr *)&servaddr,sizeof(servaddr))==-1)

{

perror("connect fail");

exit(1);

}

/* read the current term mode */

if (tty_getmode(0, &cli_termio) < 0)

perror("Error while getting client terminal mode");

/* send client termio to server rec process */

if (write(sd, &cli_termio, sizeof(cli_termio)) < 0)

perror("Error while sending client termio");

/* set input to raw mode */

if (tty_raw(0) < 0)

perror("tty_raw error");

pass_all(sd);

/* reset input back to normal */

if (tty_reset(0) < 0)

perror("tty_reset err");

close(sd);

return 0;

}

void pass_all(int fd)

{

int maxfdp1, nfound, nread;

char buff[BUFFSIZE];

fd_set readmask;

FD_ZERO(&readmask);

for ( ; ; )

{

FD_SET(0, &readmask);

FD_SET(fd, &readmask);

maxfdp1 = fd + 1;

nfound = select(maxfdp1, &readmask,NULL,NULL, (struct timeval *) 0);

if (nfound < 0)

perror("select error");

/*read from stdin and write to socket descriptor*/

if (FD_ISSET(0, &readmask))

{

nread = read(0, buff, BUFFSIZE);

if (nread < 0)

perror("read error from stdin");

else if (nread == 0)

break;

if (write(fd, buff, nread) != nread)

perror("writen error to stream pipe");

}

/*read from socket descriptor and write to std output*/

if (FD_ISSET(fd, &readmask))

{

nread = read(fd, buff, BUFFSIZE);

if (nread <= 0)

break;

if (write(1, buff, nread) != nread)

perror("write error to stdout");

}

}

}

/*

* Put a terminal device into RAW mode with ECHO off.

* Before doing so we first save the terminal's current mode,

* assuming the caller will call the tty_reset() function

* (also in this file) when it's done with raw mode.

*/

int tty_raw(int fd)             /* of terminal device */

{

struct termio   temp_mode;

if (ioctl(fd, TCGETA, (char *) &temp_mode) < 0)

return(-1);

tty_mode = temp_mode;           /* save for restoring later */

temp_mode.c_iflag  = 0;         /* turn off all input control */

temp_mode.c_oflag &= ~OPOST;    /* disable output post-processing */

temp_mode.c_lflag &= ~(ISIG | ICANON | ECHO | XCASE);

/* disable signal generation */

/* disable canonical input */

/* disable echo */

/* disable upper/lower output */

temp_mode.c_cflag &= ~(CSIZE | PARENB);

/* clear char size, disable parity */

temp_mode.c_cflag |= CS8;       /* 8-bit chars */

temp_mode.c_cc[VMIN]  = 1;      /* min #chars to satisfy read */

temp_mode.c_cc[VTIME] = 1;      /* 10'ths of seconds between chars */

if (ioctl(fd, TCSETA, (char *) &temp_mode) < 0)

return(-1);

return(0);

}

/*

* Restore a terminal's mode to whatever it was on the most

* recent call to the tty_raw() function above.

*/

int tty_reset(int fd)           /* of terminal device */

{

if (ioctl(fd, TCSETA, (char *) &tty_mode) < 0)

return(-1);

return(0);

}

/*

* Get a copy of the tty modes for a given file descriptor.

* The copy is then used later by tty_setmode() below.

*/

int tty_getmode(int fd, struct termio *tty_termio)

{

if (ioctl(fd, TCGETA, (char *) tty_termio) < 0)

return(-1);

return(0);

}

/*

* Set the tty modes for a given file descriptor.

* We set the modes from the values saved by tty_getmode() above.

*/

int tty_setmode(int fd, struct termio *tty_termio)

{

if (ioctl(fd, TCSETA, (char *) tty_termio) < 0)

return(-1);

return(0);

}